# Text boxes

TENT ERECTION INSTRUCTIONS

Inner Pitching First

- Assemble poles on ground.  5 poles: 2 longer diagonal poles (A) and (B), 1 medium cross pole (C), 2 shorter porch poles – 1 each side (D).

- Open out inner and insert two longest poles diagonally through pole sleeves running lengthways. (A) and (B). The poles are colour coded to match corresponding pole sleeve entry point.

- Insert medium length pole (C) through pole sleeve across width and locate pole end onto pin system.  The pole is colour coded to match corresponding pole sleeve entry point.

- Push pole into arch from opposite side and locate pole end onto corresponding pin system.

- Locate two longer diagonal pole ends (A) and (B) onto pin system and push poles into arch, one at a time, from opposite side. Insert pole ends onto corresponding pin system to form inner tent.

- The inner tent should now be freestanding. (Reposition if required).

- Peg the inner tent through the metal rings at the pole bases using the pin-pegs and ensuring that the groundsheet is correctly tensioned (groundsheet inside inner tent should be flat).

- IMPORTANT: It is best to peg the corner pegging point at base of each doorway before pegging the remaining metal rings of the inner tent.

## STEALTH 200, 300 & 400

# Outer Flysheet

- Open the flysheet and position so that entrance corresponds with inner doorway. Note that both entrances are the same size and shape.

- Pull flysheet over inner tent and position the seams to correspond with the poles on the inner tent.

- Fabric ties are located on the inside of the flysheet. There is one in the top centre and others around the mid-sides. These must be attached around the pole crossover points by using a simple “bow” knot.

- Insert remaining porch poles (D) to both porches through pole sleeves on the underside of the flysheet. The poles are colour coded to match corresponding pole sleeve entry point.

- Hooks around the base of the flysheet are attached to the metal rings at the pole bases.

- Peg out the two anchor straps on the porch area of one side of the tent using the V-pegs supplied. Repeat this for other porch.

- The anchor straps can be adjusted as required to ensure that the flysheet remains taut in all conditions. Regulate to suit conditions.

- Care should be taken to avoid over tension of the anchor straps as undue stress may cause damage to the flysheet fabric.

- Peg out all remaining shock-cord pegging points around the base of the flysheet.

- Peg our ALL guy lines using alloy pin-pegs ensuring that guy line fabric attachment points are evenly tensioned.

- The detachable porch groundsheet is fitted by means of elasticised hooks and pegging eyelets.